364 EDWARD STREET WAGGA WAGGA NSW 2650

PHONE 02 69 254 348 FAX 02 69 253 314

AN AUSTRALIAN DISTRIBUTOR FOR SCHWITZER TURBOCHARGERS AND EQUIPMENT

## TOYOTA HZ80 SERIES

FITTING INSTRUCTIONS

##### AS AT 18/11/08

- Remove aircleaner assembly for accessibility, refit when kit installed.

- Remove all the original exhaust system including manifold.

- Fit 2 new manifold gaskets. (if required)

- Fit turbo and manifold assy using original 2 cylinder manifold but without inner sleeve. Refit original manifold Heatshield to new manifold.

- Drain oil and remove oil level switch from the side of the sump then remove sump.

- Mark sump for oil return, drill and weld so as to line up with turbo oil drain. Refit sump and connect oil drain to turbo using small piece of ¾ hose and clamps provided. Refill the sump with oil. Fit oil line support bracket and clamp to rear bolt on air crossover pipe flange. Fit large clamp to breather tube to locate oil hose.

- Remove oil sender near starter motor and replace with items 27, 28, 29. Refit oil sender to top of T but backing slightly. Now connect oil to turbo with flex oil hose.

- Connect turbo outlet to engine crossover pipe using 2 & 2 ¾ turbo hoses and cast HZ001 turbo air out pipe.

- Fit 2 ¾ turbo hose 2” long to inlet of the turbo charger then fit HZ03 cast elbow with the short end facing turbo charger. Fit convoluted hose to HZ03 casting and HZ2A casting and fit 2 ¾ turbo hose 2” long to Air Cleaner.

- Remove engine breather rubber pipe from rocker cover and crossover pipe and discard. Blank cross over pipe breather with 5/8 cap plug and hose clamp. Now join rocker cover breather to HZ03 cast intake pipe using 5/8 oil re. Hose provided.

- Connect turbo exhaust dump pipe to turbine using V clamp. Allow clearance between chassis and inner guard.

- Fit mounting brackets in sequence.

- Fit flex pipe to dump pipe.

- Fit the rest of the exhaust system in sequence from front ensuring clearance around pipes. The muffler sits under the original Heatshield before second mount.

- When you are satisfied the exhaust alignment is correct, tighten all clamps and mounts, check.

- Fit boost gauge and pyrometer.

- Start engine and allow it to idle for 5 minutes after oil pressure has been attained and check for leaks.

- Dyno or road test vehicle and adjust maximum boost to 60KPA under full load by adjustment of actuator rod.

- Adjust maximum fuel screw to obtain a maximum of 500°C exhaust under full load at the pyrometer.

#### WARNING TO ALL FITTING STATIONS

INSTALLATION OF DIESEL TURBOCHARGER EMISSION CONTROL SYSTEMS SHOULD NOT BE UNDERTAKEN UNLESS YOU HAVE A BOOST GUAGE OR PYROMETER.

ALL DENCO DIESEL TURBO SYSTEMS RUN AT 60 KPA BOOST MAXIMUM AND A MAXIMUM OF 500°C UNDER POWER LOAD UNLESS OTHERWISE STATED.

REMEMBER: OVER FUELING NOT ONLY CAUSES BLACK SMOKE IT ALSO GENERATES EXCESS HEAT. EXCESS HEAT CAN ALSO BE CAUSED BY AIR AND EXHAUST RESTRICTIONS SO CHECK ALL AIR CLEANERS AND DUCTING TO THEM FOR RESTRICTION BEFORE TESTING. EXHAUST BRAKES AND EXHAUST SYSTEMS SHOULD ALSO BE CHECKED FOR CORRECT OPERATION AND RESTRICTION.

EXCESS HEAT CASUES MANY PROBLEMS INCLUDING HIGH N°X EMISSIONS, LAMINATION OF TURBINE HOUSING AND MANIFOLD, STUD STRETCH AND PREMATURE ENGINE FAILURE.

DENCO DIESEL WILL NOT ACCEPT LIABILITY FOR ANY PARTS RETURNED FOR WARRANTY THAT SHOWS ANY OF THE ABOVE SIGNS.

WARRANTY WILL NOT BE CONSIDERED IF REPAIRS ARE CARRIED OUT WITHOUT DENCO DIESELS AUTHORISATION.

ALL KITS NOW HAVE DUMP PIPES WITH THE PROVISION FOR VDO PYROMETERS.

REMEMBER: IF SET CORRECTLY OUR PRODUCT IS ENVIRONMENTALLY FRIENDLY AND SAFER TO THE ENVIRONMENT THAN PETROL ENGINES.

PARTS LIST DENCO DIESEL AND TURBO TOYOTA HZ80

| NO | QTY | PART NO | BIN NO | DESCRIPTION | CHECK |
| --- | --- | --- | --- | --- | --- |
| 1 | 1 | 318276-51 |  | Schwitzer S2A turbocharger with hi-flow turbine housing |  |
| 2 | 1 | TDM312 |  | Denco Diesel twin pulse manifold |  |
| 3 | 4 | RRP | X30 | 1 x 3/8 studs |  |
| 4 | 4 | 826.6212 | X6 | 1x3/8 nuts |  |
| 5 | 1 | 3LD1 | X21 | Bronze oil in fitting |  |
| 6 | 1 | SP8-450504 | T18R | ¼ BSP x 5/16 fitting* 45° |  |
| 7 | 4 | 826.0651 | X13 | 8mm x 20mm bolt |  |
| 8 | 4 | 826.7170 | X10 | 8mm spring washer |  |
| 9 | 1 | TDM106 | S8 | 1HZ oil out pipe |  |
| 10 | 1 | 6020-002 | H19 | V clamp (exhaust out) |  |
| 11 | 2 | DSF82 | S7 | Manifold gasket |  |
| AIR IN |  |  |  |
| 12 | 1 | 670-275 | V5 | 2 “ x 2 ¾” Turbo hose |  |
| 13 | 2 | HS44 | HCB12 | No 44 hose clamps |  |
| 14 | 2 | HS44 | HCB12 | No 44 hose clamps |  |
| 15 | 1 | HZ03 | S13 | Cast elbow with breather fittings |  |
| 16 | 1 | TDHZ002A | S14 | Cast elbow |  |
| 17 | 1 | 670275 | V5 | 2 ” of 2 ¾ turbo hose |  |
| 18 | 1 | 17881.54420 |  | Convoluted hose |  |
| 19 | 2 | HS44 | HCB12 | No 44 Hose clamp |  |
| AIR OUT |  |  |  |
| 20 | 1 | 670-200 | V2 | 2 1/2” x 2” turbo hose |  |
| 21 | 2 | HS032P | HCB9 | No 32 hose clamp |  |
| 22 | 1 | 670-275 | V5 | 2 1/2 “ x 2 ¾” turbo hose |  |
| 23 | 2 | HS44 | HCB12 | No 44 hose clamp |  |
| 24 | 1 | HZ001A | S12 | Cast turbo air out pipe (TDM198) |  |
| 25 | 1 | A64-02 | T13 | Boost gauge plug |  |
| OIL IN |  |  |
| 26 | 1 | TDM005 |  | Oil line support bracket |  |
| 27 | 1 | A35-02 | T14F | 1/8 BSP brass T piece |  |
| 28 | 1 | A8-0502 | T16R | 1/8 BSP x 90° - 5 fitting |  |
| 29 | 1 | A27-02 | T15F | 1/8 x 1/8 BSP straight fitting |  |
| 30 | 1 | HOS32 | H19 | Oil supply hose |  |
| 31 | 2 | 0542 12 15 | H4 | 12 * 15 pipe clamps |  |
| 32 | 1 | 0542 18 15 | H4 | 18 * 15 pipe clamps |  |
| 33 | 1 | 0057 6 12 | C12 | 13 * 5mm bolts |  |
| 34 | 1 | 826.6034 | C12 | 6mm Nyloc nuts |  |
| 35 | 1 | 36,805 | C12 | 5mm Nyloc nuts |  |
| 36 | 1 | 826.0602 | U47 | 20 * 6mm bolts |  |
| OIL OUT |  |  |  |
| 37 | 1 | TDM107 | S2 | 1 HZ oil out elbow sump |  |
| 38 | 1 | LOL-12 |  | 6” of ¾ “ turbo hose |  |
| 39 | 2 | HS10 | HCB5 | No 10 hose clamp |  |
| 40 | 1 | FS6069 | B12 | 5/8 cap plug |  |
| 41 | 3 | HS10 | HCB5 | No 10 hose clamp |  |
| 42 | 1 | LOL-10 |  | 5/8” oil hose x 17” long |  |

| EXHAUST OUT |  |  |  |
| --- | --- | --- | --- |
| 43 | 1 | TDM108 | R5 | Turbo exhaust dump pipe |  |
| 44 | 1 | TDM450 |  | HZ 80 flex pipe |  |
| 45 | 1 | TDM109 | D19 | Bracket Clamp |  |
| 46 | 1 | DDHZ80-4MB | R8 | Pipe |  |
| 47 | 1 | TR616CC250-GP |  | 2 ½ muffler |  |
| 48 | 1 | TDM110 | D20 | Bracket clamp |  |
| 49 | 1 | DDHZ80-5MB | R6 | Pipe |  |
| 50 | 1 | DDHZ80-6MB | R10 | Pipe |  |
| 51 | 1 | DDHZ80-7MB | R9 | Pipe |  |
| 52 | 1 | TDM114 | D21 | Bracket clamp |  |
| 53 | 6 | C12 | W11 | Exhaust clamp |  |

PICKING LIST HZ80

| NO | QTY | PART NO | BIN NO | DESCRIPTION |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 1 | 318276-51 |  | Schwitzer S2A turbocharger with hi-flow turbine housing |  |  |  |  |  |  |
| 2 | 1 | TDM312 |  | Denco Diesel twin pulse manifold |  |  |  |  |  |  |
| 3 | 4 | RRP | X30 | 1 x 3/8 studs |  |  |  |  |  |  |
| 4 | 4 | 8266212 | X6 | 1x3/8 nuts |  |  |  |  |  |  |
| 5 | 1 | 3LD1 | X21 | Bronze oil in fitting |  |  |  |  |  |  |
| 6 | 1 | SP8-450504 | T18R | ¼ BSP x 5/16 fitting* 45° |  |  |  |  |  |  |
| 7 | 4 | 8260651 | X13 | 8mm x 20mm bolt |  |  |  |  |  |  |
| 8 | 4 | 8267170 | X10 | 8mm spring washer |  |  |  |  |  |  |
| 9 | 1 | TDM106 | S8 | 1HZ oil out pipe |  |  |  |  |  |  |
| 10 | 1 | 6020002 | H19 | V clamp (exhaust out) |  |  |  |  |  |  |
| 11 | 2 | DSF82 | S7 | Manifold gasket |  |  |  |  |  |  |
| AIR IN |
| 12 | 1 | 670-275 | V5 | 2 “ x 2 ¾” Turbo hose |  |  |  |  |  |  |
| 13 | 2 | HS44 | HCB12 | No 44 hose clamps |  |  |  |  |  |  |
| 14 | 2 | HS44 | HCB12 | No 44 hose clamps |  |  |  |  |  |  |
| 15 | 1 | HZ03 | S13 | Cast elbow with breather fittings |  |  |  |  |  |  |
| 16 | 1 | TDHZ002A | S14 | Cast elbow |  |  |  |  |  |  |
| 17 | 1 | 670275 | V5 | 2 ” of 2 ¾ turbo hose |  |  |  |  |  |  |
| 18 | 1 | 17881.54420 |  | Convoluted hose |  |  |  |  |  |  |
| 19 | 2 | HS44 | HCB12 | No 44 Hose clamp |  |  |  |  |  |  |
| AIR OUT |
| 20 | 1 | 670-200 | V2 | 2 1/2” x 2” turbo hose |  |  |  |  |  |  |
| 21 | 2 | HS032P | HCB9 | No 32 hose clamp |  |  |  |  |  |  |
| 22 | 1 | 670-275 | V5 | 2 1/2 “ x 2 ¾” turbo hose |  |  |  |  |  |  |
| 23 | 2 | HS44 | HCB12 | No 44 hose clamp |  |  |  |  |  |  |
| 24 | 1 | HZ001A | S12 | Cast turbo air out pipe (TDM198) |  |  |  |  |  |  |
| 25 | 1 | A64-02 | T13 | Boost gauge plug |  |  |  |  |  |  |
| OIL IN |
| 26 | 1 | TDM005 |  | Oil line support bracket |  |  |  |  |  |  |
| 27 | 1 | A35-02 | T14F | 1/8 BSP brass T piece |  |  |  |  |  |  |
| 28 | 1 | A8-0502 | T16R | 1/8 BSP x 90° - 5 fitting |  |  |  |  |  |  |
| 29 | 1 | A27-02 | T15F | 1/8 x 1/8 BSP straight fitting |  |  |  |  |  |  |
| 30 | 1 | HOS32 | H19 | Oil supply hose |  |  |  |  |  |  |
| 31 | 2 | 0542 12 15 | H4 | 12 * 15 pipe clamps |  |  |  |  |  |  |
| 32 | 1 | 0542 18 15 | H4 | 18 * 15 pipe clamps |  |  |  |  |  |  |
| 33 | 1 | 0057 6 12 | C12 | 13 * 5mm bolts |  |  |  |  |  |  |
| 34 | 1 | 826.6034 | C12 | 6mm Nyloc nuts |  |  |  |  |  |  |
| 35 | 1 | 36,805 | C12 | 5mm Nyloc nuts |  |  |  |  |  |  |
| 36 | 1 | 826.0602 | U47 | 20 * 6mm bolts |  |  |  |  |  |  |
| OIL OUT |
| 37 | 1 | TDM107 | S2 | 1 HZ oil out elbow sump |  |  |  |  |  |  |
| 38 | 1 | LOL-12 |  | 6” of ¾ “ turbo hose |  |  |  |  |  |  |
| 39 | 2 | HS10 | HCB5 | No 10 hose clamp |  |  |  |  |  |  |
| 40 | 1 | NG-FS6069 | B12 | 5/8 cap plug |  |  |  |  |  |  |
| 41 | 3 | HS10 | HCB5 | No 10 hose clamp |  |  |  |  |  |  |
| 42 | 1 | LOL-10 |  | 5/8” oil hose x 17” long |  |  |  |  |  |  |
| EXHAUST OUT |
| 43 | 1 | TDM108 | R5 | Turbo exhaust dump pipe |  |  |  |  |  |  |
| 44 | 1 | TDM450 |  | HZ 80 flex pipe |  |  |  |  |  |  |
| 45 | 1 | TDM109 | D19 | Bracket Clamp |  |  |  |  |  |  |
| 46 | 1 | DDHZ80-4MB | R8 | Pipe |  |  |  |  |  |  |
| 47 | 1 | TR616CC250-GP |  | 2 ½ muffler |  |  |  |  |  |  |
| 48 | 1 | TDM110 | D20 | Bracket clamp |  |  |  |  |  |  |
| 49 | 1 | DDHZ80-5MB | R6 | Pipe |  |  |  |  |  |  |
| 50 | 1 | DDHZ80-6MB | R10 | Pipe |  |  |  |  |  |  |
| 51 | 1 | DDHZ80-7MB | R9 | Pipe |  |  |  |  |  |  |
| 52 | 1 | TDM114 | D21 | Bracket clamp |  |  |  |  |  |  |
| 53 | 6 | C12 | W11 | Exhaust clamp |  |  |  |  |  |  |